## Slide 1: IK2227 – Lab 1: Routing
Slides by: M. Scazzariello
Contributions by: L. Ariemma, T. Caiazzi, G. Di Battista, M. Patrignani

## Slide 2: Fat-Tree data center topology
the Fat-Tree is a special case of a Clos
typical Fat-Tree architectures today consist of three level of nodes (switches/routers)
high redundancy
typically, nodes have the same characteristics
  easier to stock spare equipment

## Slide 3: why BGP in Fat-Trees?
BGP has several stable and robust implementations, even open-source
  e.g., FRRouting, Quagga
BGP generates less flooding than common IGPs (IS-IS, OSPF, etc.)
  if a received update does not change the best route, a BGP speaker does not propagate the update
BGP natively supports ECMP (Equal-Cost Multi-Path)
  Fat-Trees have many paths with the same length

## Slide 4: (recap) the two modes of BGP
BGP can work in two modes:
  eBGP (external BGP): interconnects networks owned by different administrative domains (i.e., different companies)
    identified by different ASNs
  iBGP (internal BGP): interconnects border routers within the same AS (i.e., routers of the same company)
    they all share the same ASN

## Slide 5: why using eBGP? (and not iBGP)
the most obvious choice would be to use iBGP since the data center network is under the same administration
however, eBGP is always used because
  eBGP is easier to setup, no need for IGP
    with iBGP, the IGP would compute routes
  iBGP multipath support has some limitations
    can be overcame, but it is complex

## Slide 6: inter-domain routing VS DC routing
inter-domain routing | data centers’ routing
the internet has relatively sparse connectivity | data centers’ networks have very dense connectivity
stability is preferred over quick convergence | quick convergence is preferred over stability
the aim is computing a single best path for each destination | the aim is computing multiple paths to each destination

## Slide 7: BGP in the data center
BGP was primarily devised for inter-domain routing
  default configurations are not suitable in a data center
needs some tweaks described in RFC 7938
  AS numbers assignment
  ECMP policy relax
  timer adjustment

## Slide 8: AS numbers assignment
global ASNs are not used in the data center
  they can be misleading
    because operators associate them with names
  they are dangerous
    an accidental leakage of the internal BGP notifications to the Internet may be disruptive
private ASNs are generally used
  the 2-byte ASNs allow only 1,023 private ASes in the range 64512–65534
  the 4-byte ASNs support almost 95 million private ASes

## Slide 9: ASes and routers
the most obvious choice would be assigning a different ASN to each node
however, this approach would lead to BGP path exploration issues

## Slide 10: BGP path exploration
immediately after a fault there is a transient period when inconsistent AS-paths are propagated in the network
  routers have plenty of alternatives and jump from one to another before all alternatives are withdrawn
  each best route change is propagated again by the routers
  lots of useless BGP updates are transmitted
since data centers’ topologies are dense and hence have a lot of cycles this problem must be addressed

## Slide 11: the RFC’s AS scheme
each Leaf is a different AS
the Spine nodes of each PoD belong to the same AS
the Core nodes of the same plane belong to the same AS

## Slide 12: the RFC’s ASes scheme – multi-plane
Server Farm
Plane A
Plane B

## Slide 13: BGP and ECMP
BGP natively supports ECMP
  reminder: ECMP is a hash-based load-balancing mechanism! 
by default, BGP considers two announcement of the same prefix “equal” if they are equal in each best-path selection criterion except for the last one
  lowest router-id of the announcing peer
to enable multi-path, BGP requires that the AS-paths selected for multi-path match exactly
  not just they have equal-length but equal AS numbers inside

## Slide 14: BGP multi-path relax
when the AS_PATH lengths of different announcements for the same prefix are the same, the best-path algorithm skips checking for exact match of the AS numbers
this modification is often called “as-path multipath-relax”
  different vendors may use different names

## Slide 15: tuning BGP timers
there are four main timers that are responsible for BGP behaviour
  advertisement interval timer
  keepalive timer
  hold timer
  connect timer

## Slide 16: advertisement interval timer
announcements that need to be sent to a neighbor are “bundled” and sent together only when the interval expires
  then the timer is reset for that neighbor
the default value for eBGP is 30s
  in interdomain routing this improves stability and reduces the number of multiple updates for the same prefix
in data centers is set to 0s
  required for fast convergence

## Slide 17: keepalive and hold timers
each BGP peer sends periodic keepalive messages to its neighbors according to the keepalive timer
when a peer does not receive a keepalive for a period greater than the hold timer
  the connection is dropped
  all the announcements received are considered invalid
  the peer tries to re-establish the connection
by default, the keepalive timer is 60s and the hold timer is 180s
in data centers timers of 3s and 9s are used, respectively

## Slide 18: connect timer
when a connection to a peer fails, BGP waits for the connect timer expiration before attempting to reconnect
  the connect timer by default is 60s
  this can delay session re-establishment when a link recovers from a failure or a node powers up
in data centers, it is set to 10s

## Slide 19: automating the configuration
unnumbered interfaces
  used to establish peerings specifying the interface name rather than the IP address and the remote AS number
peer groups
  used to specify policies for groups of peers

## Slide 20: lab deep dive

## Slide 21: lab pre-conditions
Linux and macOS
  no specific requirement
Windows
  currently, the WSL 2 kernel does not have Multi-Path enabled
  need to fallback to Hyper-V Docker backend
    open Docker Desktop and go to Settings (cog in the top-right corner)
    unselect the “Use the WSL 2 based engine” checkbox
    click “Apply & restart”
  Hyper-V is only supported on the Pro version
    if you have the Home version, you can download the VM from Canvas

## Slide 22: a primer on IPv6 addresses
IPv6 is the successor of IPv4
  several changes from its predecessor
  one of these changes is the IP address length
    a IPv4 address length is 32 bits (4 Bytes)
    a IPv6 address length is 128 bits (16 Bytes)
important difference: a single host can be identified by multiple IPv6 addresses (of different types)
IPv4 and IPv6 can coexist on the same interface!

## Slide 23: types of unicast IPv6 address
important difference: a single host can be identified by multiple IPv6 addresses (of different types)
main types of (unicast) IPv6 address:
  global: publicly reachable and routed on the Internet
  link-local: auto-generated from the MAC address
    only used for addressing at the link level (i.e., segment or LAN)
  unique-local: can be routed except on the Internet
    used to interconnect different LANs (e.g., different buildings)

## Slide 24: lab pre-conditions
FRRouting handles unnumbered interfaces by using IPv6 link-local addresses
  all the routers in the fabric must have IPv6 enabled
    in Kathará, to enable IPv6 for machine router, add router[ipv6]="True" in the lab.conf file
    in the lab, IPv6 is already enabled for all the routers

## Slide 25: naming convention
core_x_y
  x: plane number, 1 in this case
  y: Core number
spine_x_y
  x: PoD number
  y: Spine number
leaf_x_y
  x: PoD number
  y: Leaf number
server_x_y_z
  x: PoD number
  y: Leaf number
  z: server number

## Slide 26: task 1: complete the Fat-Tree
spine_1_1
leaf_1_1
leaf_1_2
spine_2_1
spine_2_2
core_1_1
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
201.1.1.0/24
201.1.2.0/24
201.2.2.0/24
201.2.1.0/24
202.2.2.0/24
202.2.1.0/24
I
G
H
J
202.1.1.0/24
202.1.2.0/24
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
3
2
1
0
0
1
2
3
0
1
2
3

## Slide 27: Core configuration example
router bgp 64518
timers bgp 3 9
bgp router-id 192.168.0.14
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor SPINES peer-group
neighbor SPINES remote-as external
neighbor SPINES advertisement-interval 0
neighbor SPINES timers connect 10
neighbor eth0 interface peer-group SPINES
neighbor eth1 interface peer-group SPINES
neighbor eth2 interface peer-group SPINES
neighbor eth3 interface peer-group SPINES
address-family ipv4 unicast
neighbor SPINES activate
maximum-paths 64
exit-address-family
bgpd.conf
set keepalive and hold timers
BGP multi-path relax
create a peer-group
all peers of the group are eBGP. The remote ASN is inferred
set advertisement interval timer
set connect timer
add interfaces to peer-group for unnumbered peering
enable A.F. to peer-group
maximum Multi-Path possibilities

## Slide 28: Spine configuration example
router bgp 64514
timers bgp 3 9
bgp router-id 192.168.0.5
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor LEAFS peer-group
neighbor LEAFS remote-as external
neighbor LEAFS advertisement-interval 0
neighbor LEAFS timers connect 10
neighbor eth0 interface peer-group LEAFS
neighbor eth1 interface peer-group LEAFS
neighbor CORES peer-group
neighbor CORES remote-as external
neighbor CORES advertisement-interval 0
neighbor CORES timers connect 10
neighbor eth2 interface peer-group CORES
neighbor eth3 interface peer-group CORES
bgpd.conf – part 1
address-family ipv4 unicast
neighbor CORES activate
neighbor LEAFS activate
maximum-paths 64
exit-address-family
bgpd.conf – part 2

## Slide 29: Leaf configuration example
router bgp 64512
timers bgp 3 9
bgp router-id 192.168.0.1
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor SPINES peer-group
neighbor SPINES remote-as external
neighbor SPINES advertisement-interval 0
neighbor SPINES timers connect 10
neighbor eth0 interface peer-group SPINES
neighbor eth1 interface peer-group SPINES
address-family ipv4 unicast
neighbor SPINES activate
network 201.1.1.0/24 network 201.1.2.0/24
maximum-paths 64
exit-address-family
bgpd.conf
announce the server prefixes

## Slide 30: task 1: complete the Fat-Tree
spine_1_1
leaf_1_1
leaf_1_2
spine_2_1
spine_2_2
core_1_1
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
201.1.1.0/24
201.1.2.0/24
201.2.2.0/24
201.2.1.0/24
202.2.2.0/24
202.2.1.0/24
I
G
H
J
202.1.1.0/24
202.1.2.0/24
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
3
2
1
0
0
1
2
3
0
1
2
3
add the missing machines (spine_1_2, core_1_2, and leaf_2_1) in the lab.conf file
  the proper metadata (IPv6, multipath, image) are already declared
  define the machine interfaces (follow the grey numbers in the figure! )
write their “.startup” files and their FRRouting configurations
  hint: most of the configuration is symmetric, you might “take a look” to similar machines and adjust it!
  hint 2: to assign the router-id, pick a unique 192.168.0.x address for each node
announce the missing prefix (red box) in leaf_2_2

## Slide 31: start the lab
open a terminal
enter the lab directory (cd lab_directory)
run kathara lstart

## Slide 32: task 2: analyzing routing
verify that the topology is configured correctly
let’s focus on core_1_2
  how many prefixes are received/installed in the routing table?
    how many ECMP next-hops does each received prefix have?
    which IP version are the next-hops? Can you tell why?
let’s focus on leaf_2_1
  how many prefixes are received/installed in the routing table?
verify the same for the routing table of spine_1_2

## Slide 33: a nice detail
on leaf_1_1, run:
  ip address show eth3
IPv4 and IPv6 are coexisting!
  can you tell which type of IPv6 address is that?

## Slide 34: task 3: analyzing a failure
assume that, for some reason, the node spine_1_2 fails
  to destroy a single machine in a lab, run:
    kathara lclean <machine_name>
    in this case: kathara lclean spine_1_2
what happens to the routing table of all the Spines and Cores?
is there any change in the routing table of leaf_1_1 and leaf_1_2? Why?
what about the routing table of leaf_2_1? Why?

## Slide 35: task 3: analyzing a failure
after analyzing the failure, restore spine_1_2
  to start a single machine in a lab, run:
    kathara lstart <machine_name>
    in this case: kathara lstart spine_1_2

## Slide 36: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
our source is server_1_1_2 and our destination is server_2_2_2

## Slide 37: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
our source is server_1_1_2 and our destination is server_2_2_2
spine_1_1
leaf_1_1
leaf_1_2
spine_2_1
spine_2_2
core_1_1
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
spine_1_2
leaf_2_1
core_1_2

## Slide 38: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
our source is server_1_1_2 and our destination is server_2_2_2
we start two sniffers in the downward path
spine_1_1
leaf_1_1
leaf_1_2
spine_2_1
spine_2_2
core_1_1
server_1_1_1
server_1_1_2
server_1_2_1
server_1_2_2
server_2_1_1
server_2_1_2
server_2_2_1
server_2_2_2
leaf_2_2
A
C
U
V
Z
M
F
P
W
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
spine_1_2
leaf_2_1
core_1_2

## Slide 39: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
our source is server_1_1_2 and our destination is server_2_2_2
we start two sniffers in the downward path
on spine_2_1 and spine_2_2 run:
  tcpdump -i eth1 udp
name of the interface
filter only UDP traffic

## Slide 40: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
while tcpdumps are running, on server_1_1_2, run:
hping3 --udp 202.2.2.2 -s 2000 -p ++1000 -c 30
UDP mode
destination IP
starting src port value (increases per-packet)
starting dst port value
(“++” makes it increase per-packet)
# packets to send

## Slide 41: task 4: analyzing end-to-end traffic
to test the ECMP load-balancing, we send UDP packets and observe how they are distributed among the available paths
once hping has stopped, stop the tcpdumps (CTRL+C)
how many packets did each Spine receive?
  are they (almost) equally distributed?

## Slide 42: task 4: analyzing end-to-end traffic
let’s start a new tcpdump on core_1_1:
  tcpdump -i any udp
while tcpdump is running, on server_1_1_2, run:
hping3 --udp 202.2.2.2 -s 2000 -k -p 1000
This will generate a single UDP flow
dump traffic from any interface
fixed dst port value
keep src port fixed

## Slide 43: task 4: analyzing end-to-end traffic
let’s observe the output of the tcpdump on core_1_1:
  from which interface are packets coming in?
    to which Spine node does it correspond?
  from which interface are packets going downwards?
    to which Spine node does it correspond?

## Slide 44: task 4: analyzing end-to-end traffic
while running hping and tcpdump, let’s study how a failure on the link between the Spine and the Leaf affects the ECMP logic on the Core switch
on the lab terminal, run:
kathara exec <spine_name> "ip link set dev eth1 down"
  the command will administratively put the interface down

## Slide 45: task 4: analyzing end-to-end traffic
let’s observe the output of the tcpdump on core_1_1:
  after the failure, is the input interface changing?
    can you explain why?
  after the failure, is the output interface changing?
    can you explain why?

## Slide 46: task 4: analyzing end-to-end traffic
on the lab terminal, run:
kathara exec <spine_name> "ip link set dev eth1 up"
  the command will restore the interface in a working state
observe again the output of the tcpdump on core_1_1:
  after the restore, is the input interface changing?
    can you explain why?
  after the restore, is the output interface changing?
    can you explain why?

## Slide 47: stop the lab
open a terminal
enter the lab directory (cd lab_directory)
run kathara lclean