## Slide 1: IK2227 – Lab 2: Virtualization
Slides by: M. Scazzariello
Contributions by: L. Ariemma, T. Caiazzi, G. Di Battista, M. Patrignani

## Slide 2: a Fat-Tree with BGP routing
Servers
Containers or VMs
Prefixes are assigned directly to the servers
each Leaf announces its server’s prefix

## Slide 3: drawbacks of using just BGP
containers/VMs share the same IP prefix of the server
  no possibility to move containers between servers without IP remapping
tenants must follow the IP plan of the data center
  cannot expose containers with custom IPs
there is no isolation between
  the data center traffic and the tenant's traffic
  different tenants

## Slide 4: how to handle multiple tenants?

## Slide 5: servers' architecture requirements
having user services directly on bare metal is not used
  too many physical servers needed
  no way to scale if more resources are requested
  no isolation between different services on the same server
support a virtual layer of containers or VMs
  high-availability guaranteed via orchestration
  useful for resource-slicing
  isolation between different containers/VMs on the same server
    possibility to assign containers or VMs to different tenants

## Slide 6: orchestration requirements
an orchestrator is a software that manages the lifecycle of containers/VMs
  creates, moves, and destroys containers/VMs
needed for
  optimal resource allocation, handling failures, management
when moving a container/VM
  possibility to keep network configurations (MAC/IP)
  minimal downtime

## Slide 7: tenant requirements
each tenant wants to independently manage its own private IP address space
  containers/VMs traffic must be segregated between tenants and between the data center traffic

## Slide 8: consequence of requirements
server, orchestration, and tenant requirements have a consequence
  usage of tunnels

## Slide 9: tunneling protocol requirements
minimal configuration
encapsulate the traffic of each tenant
  an identifier of the tenant is needed
encapsulation in Layer-4
  to fully exploit ECMP Multi-Path
  to traverse routers
    data center fabric is Layer-3
  to traverse Internet
    different data centers must interconnect via Internet transparently (to create the so called regions)

## Slide 10: possible choices for tunneling
VLAN
  can be used only in Layer-2, the data center is Layer-3
MPLS
  each router must be configured for each new tenant
  traversing Internet requires ISP to configure intermediate routers
VXLAN
  created ad-hoc 

## Slide 11: VXLAN
Virtual eXtensible Local Area Network (RFC-7348)
designed to address the need for overlay networks within virtualized data centers accommodating multiple tenants
encapsulates Layer-2 frames into UDP packets

## Slide 12: VXLAN terminology
VNI: VXLAN Network Identifier
  identifier of a specific VXLAN tunnel
  similar to the VLAN ID
  24-bit address space, more than 16M possible VNIs
VTEP: VXLAN Tunnel End Point
  device (physical or virtual) that encapsulates and decapsulates VXLAN packets

## Slide 13: VXLAN encapsulation
overhead of 50 bytes
random Source Port to fully exploit ECMP Multi-Path

## Slide 14: MAC-to-VTEP Table
hosted in each VTEP
similar to the switch forwarding table
for each VNI the VTEP keeps a table of pairs <mac,ip>, that associates MAC Addresses and destination VTEP IPs
each physical (or VLAN) Layer-2 interface of a VTEP is assigned to a VNI
  the MAC addresses learned on such interfaces are local, and the IPs of their pairs are replaced by the word local

## Slide 15: MAC-to-VTEP Table
when a VTEP receives a frame destinated to a MAC Address m from a local interface belonging to a certain VNI, it checks for the existence (in the VNI) of a pair <m,i> containing m
  if the pair exists, the VTEP encapsulates the frame, and sends the resulting packet to the destination VTEP IP i
  if not, the frame is sent to all the other VTEPs (encapsulated) and to all the local ports of that VNI

## Slide 16: VXLAN transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
L2 Packets
VXLAN Packets, VNI 100
L2 Packets
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
.1
.2

## Slide 17: how to handle broadcast traffic
two types of broadcast must be handled
  traffic directed to the MAC broadcast address
    e.g., ARP traffic
  traffic directed to a MAC address that has not been learned
IP multicast groups are used by default
  each VNI is assigned to an IP multicast group of the underlay network and each VTEP subscribes itself to each group of its VNIs
  the multicast group of a VNI is only used to send the broadcast traffic

## Slide 18: disadvantages of multicast
multicast must be enabled in the underlay network
  it may require to deploy several protocols
    e.g., IGMP, IGMP Snooping, PIM, ….
  complex configuration
if multicast is not enabled, broadcast frames are duplicated and sent unicast to all the VTEPs of the VNI

## Slide 19: EVPN-BGP
Ethernet VPN (RFC-7432 and RFC-8365)
uses MP-BGP with specific AFI/SAFI
  Address Family Identifier/Subsequent AFI
  AFI=25 (L2VPN) – SAFI=70 (EVPN)
advertises MAC Addresses of VNIs using BGP updates
a VTEP automatically learns local MAC Addresses and advertises them to all other VTEPs (of the same VNI)

## Slide 20: VXLAN and EVPN-BGP transport
VTEP
VTEP
Host 1
Host 2
193.204.0.0/15
.1
.2
10.0.0.0/24
10.0.0.0/24
.1
0:A
.2
0:B
0:A 100 local
0:B 100 193.204.0.2
0:B 100 local
0:A 100 193.204.0.1
eBGP multihop peering
0:A 100 local
0:A 100 193.204.0.1
0:A 100 193.204.0.1
0:B 100 193.204.0.2
0:B
0:A
(+ BGP Router)
(+ BGP Router)

## Slide 21: putting everything together

## Slide 22: lab topology
AF
AA
AB
spine_1_2
spine_1_1
spine_2_1
spine_2_2
core_1_1
core_1_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_1
leaf_2_2
A
C
Z
W
M
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
lo: 192.168.0.2/32
leaf_1_2
leaf_1_1
lo: 192.168.0.4/32
lo: 192.168.0.1/32
lo: 192.168.0.3/32
VNI: 5010, VLAN ID 10
Prefix: 10.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 10.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 10.30.0.0/16

## Slide 23: where is the VTEP?
containers must be unaware of tunneling
different choices for positioning the VTEP
  in each server
    the server should have a BGP peering for enabling EVPN-BGP
    the server CPU would be used to route packets
  in each Leaf
    a Leaf already has a BGP peering (for the underlay network)
    a Leaf is a router, so it has dedicated routing hardware
    usage of VLANs in the link connecting a Leaf and a server to distinguish tenants

## Slide 24: inside the Leaves
VLANs are used
mapping between VNIs and VLAN IDs
  tenants are unaware of the mapping
when receiving a packet: Leaves decapsulate VXLAN and encapsulate into VLAN frames, according to the mapping
when sending a packet: Leaves decapsulate VLAN frames and encapsulate into VXLAN, according to the mapping

## Slide 25: inside the servers
the server uses the VLAN IDs to forward packets to the correct containers/VMs sub-networks
  containers/VMs of the same tenant share the same virtual Layer-2 network
the server untags the packets so that the containers/VMs are unaware of the VLANs

## Slide 26: deploying VXLAN
AF
AA
AB
spine_1_2
spine_1_1
spine_2_1
spine_2_2
core_1_1
core_1_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_1
leaf_2_2
A
C
Z
W
M
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
leaf_1_2
leaf_1_1
VXLAN
VLAN
no encapsulation
VNI: 5010, VLAN ID 10
Prefix: 10.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 10.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 10.30.0.0/16
VLAN ID VNI
10 5010
20 5020
… …
VLAN ID Container
10 1_1_1
10 1_1_2
20 1_1_3
… …

## Slide 27: configuring Leaves
we need to configure the Leaf in order to:
  act as a bridge on Layer-2 ports (toward servers)
    able to perform Layer-2 learning
  act as a router on the ports of the data center (towards spines)
    able to establish BGP peerings
    able to encapsulate/decapsulate VXLAN traffic

## Slide 28: configuring Leaves - VTEP configuration
create bridge facilities (aka companion bridges)
  attach the tenant’s collision domains to the companion bridge
configure the base BGP peerings
  enable the AFI/SAFI of EVPN
configure VXLAN

## Slide 29: configuring Leaves - companion bridge
the bridge connected to VTEP interfaces
  used by the VTEP to perform source address learning of local interfaces (the tenants’ ones)
when in combination with EVPN-BGP
  its forwarding table is also populated via updates from BGP
  the FRR control plane watches updates of the bridge forwarding table to send updates via BGP

## Slide 30: leaf configuration example – part 1
# Configure loopback
ip address add 192.168.0.1/32 dev lo
ip route add 192.168.0.1/32 dev lo
# Setting up VXLAN interfaces
ip link add vtep5010 type vxlan id 5010 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link add vtep5020 type vxlan id 5020 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link add vtep5030 type vxlan id 5030 dev lo dstport 4789 local 192.168.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
leaf_1_1.startup
configure an IP address on the loopback interface
create the interface
name of the interface
VNI
VXLAN dst port
VXLAN src IP, set to the loopback IP
disable the mcast learning
send VXLAN packets via loopback interface

## Slide 31: leaf configuration example – part 1
# Configure loopback
ip address add 192.168.0.1/32 dev lo
ip route add 192.168.0.1/32 dev lo
# Setting up VXLAN interfaces
ip link add vtep5010 type vxlan id 5010 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link add vtep5020 type vxlan id 5020 dev lo dstport 4789 local 192.168.0.1 nolearning
ip link add vtep5030 type vxlan id 5030 dev lo dstport 4789 local 192.168.0.1 nolearning
# Creating the companion bridge
ip link add br100 type bridge
ip link set br100 addrgenmode none
leaf_1_1.startup
create the companion bridge and name it
disable IPv6 link-local generation on the bridge

## Slide 32: leaf configuration example – part 2
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge VLANs
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
bridge vlan add vid 30 dev eth2
leaf_1_1.startup – part 2
attach the VTEP to the companion bridge
do not generate IPv6 link-local addresses

## Slide 33: leaf configuration example – part 2
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge VLANs
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
bridge vlan add vid 30 dev eth2
leaf_1_1.startup – part 2
set the type of vtep5010 to bridge_slave
suppress neighbor discovery (ARP and ND)
do not learn MAC addresses

## Slide 34: leaf configuration example – part 2
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge VLANs
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
bridge vlan add vid 30 dev eth2
leaf_1_1.startup – part 2
attach eth2 (the Layer-2 collision domain towards server_1_1) to the companion bridge

## Slide 35: leaf configuration example – part 2
# Attach interfaces to the bridge
ip link set dev vtep5010 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5020 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev vtep5030 master br100 addrgenmode none
ip link set vtep5010 type bridge_slave neigh_suppress on learning off
ip link set dev eth2 master br100
# Enable bridge VLANs
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev vtep5010 pvid untagged
bridge vlan add vid 20 dev vtep5020 pvid untagged
bridge vlan add vid 30 dev vtep5030 pvid untagged
bridge vlan add vid 10 dev eth2
bridge vlan add vid 20 dev eth2
bridge vlan add vid 30 dev eth2
leaf_1_1.startup – part 2
enable VLANs on the bridge
configure the VTEP ports to receive/send untagged traffic of specific VLANs
configure the server ports to receive/send VLAN tagged traffic of specific VLANs

## Slide 36: leaf configuration example – part 3
# Enable interfaces
ip link set up dev vtep5010
ip link set up dev vtep5020
ip link set up dev vtep5030
ip link set up dev br100
systemctl start frr
leaf_1_1.startup – part 3
enable all the VTEPs
enable the companion bridge
start FRRouting

## Slide 37: leaf BGP configuration example
router bgp 64512
timers bgp 3 9
bgp router-id 192.168.0.1
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor SPINES peer-group
neighbor SPINES remote-as external
neighbor SPINES advertisement-interval 0
neighbor SPINES timers connect 10
neighbor eth0 interface peer-group SPINES
neighbor eth1 interface peer-group SPINES
bgpd.conf - part 1
address-family ipv4 unicast
neighbor SPINES activate
redistribute connected route-map LOOPBACKS
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor SPINES activate
advertise-all-vni
exit-address-family
route-map LOOPBACKS permit 10
match interface lo
bgpd.conf - part 2
route-map to announce the loopback IP
enable the l2vpn evpn AFI/SAFI A.F.

## Slide 38: server configuration example
# Creating the bridge
ip link add br100 type bridge
# Attach interfaces to the bridge
ip link set dev eth0 master br100
ip link set dev eth1 master br100
ip link set dev eth2 master br100
# Enable bridge VLANs
ip link set dev br100 type bridge vlan_filtering 1
bridge vlan add vid 10 dev eth0
bridge vlan add vid 20 dev eth0
bridge vlan add vid 10 dev eth1 pvid untagged
bridge vlan add vid 20 dev eth2 pvid untagged
ip link set up dev br100
server_1_1.startup
configure the port towards the Leaf on the bridge to receive tagged VLAN packets
configure the container ports to send untagged frames

## Slide 39: spine BGP configuration example
router bgp 64514
timers bgp 3 9
bgp router-id 192.168.0.5
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
neighbor LEAFS peer-group
neighbor LEAFS remote-as external
neighbor LEAFS advertisement-interval 0
neighbor LEAFS timers connect 10
neighbor eth0 interface peer-group LEAFS
neighbor eth1 interface peer-group LEAFS
bgpd.conf - part 1
neighbor CORES peer-group
neighbor CORES remote-as external
neighbor CORES advertisement-interval 0
neighbor CORES timers connect 10
neighbor eth2 interface peer-group CORES
neighbor eth3 interface peer-group CORES
address-family ipv4 unicast
neighbor CORES activate
neighbor LEAFS activate
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor CORES activate
neighbor LEAFS activate
exit-address-family
bgpd.conf - part 2
activate the l2vpn evpn AFI/SAFI A.F.

## Slide 40: Core BGP configuration example
router bgp 64518
timers bgp 3 9
bgp router-id 192.168.0.13
no bgp ebgp-requires-policy
bgp bestpath as-path multipath-relax
bgpd.conf - part 1
neighbor SPINES peer-group
neighbor SPINES remote-as external
neighbor SPINES advertisement-interval 0
neighbor SPINES timers connect 10
neighbor eth0 interface peer-group SPINES
neighbor eth1 interface peer-group SPINES
neighbor eth2 interface peer-group SPINES
neighbor eth3 interface peer-group SPINES
address-family ipv4 unicast
neighbor SPINES activate
maximum-paths 64
exit-address-family
address-family l2vpn evpn
neighbor SPINES activate
exit-address-family
bgpd.conf - part 2
activate the l2vpn evpn AFI/SAFI A.F.

## Slide 41: container configuration example
ip address add 10.10.0.1/16 dev eth0
ip link set dev eth0 mtu 1450
systemctl start apache2
container_1_1_1.startup
assign an IP to the container (chosen by the tenant)
reduce the interface MTU (50 bytes are taken by the VXLAN header)
another small detail in the lab.conf
...
container_1_1_1[0]="AA/00:00:00:01:01:01"
...
lab.conf
defines the MAC address for the interface

## Slide 42: lab pre-conditions
Linux and macOS
  no specific requirement
Windows
  currently, the WSL 2 kernel does not have Multi-Path enabled
  need to fallback to Hyper-V Docker backend
    open Docker Desktop and go to Settings (cog in the top-right corner)
    unselect the “Use the WSL 2 based engine” checkbox
    click “Apply & restart”
  Hyper-V is only supported on the Pro version
    if you have the Home version, you can download the VM from Canvas

## Slide 43: task 1: complete the topology
write leaf_1_2 “.startup” file and its FRRouting configuration
  it needs to be configured with VTEPs, VLANs, and EVPN-BGP
    it must be able to forward (VTEP=5020, VLAN=20) and (VTEP=5030, VLAN=30)
  hint: most of the configurations are symmetric, you might “take a look” to leaf_1_1 and adjust them!
  hint 2: the loopback address is shown in the figure
  hint 3: to assign the router-id, pick a unique 192.168.0.x address
AF
AA
AB
spine_1_2
spine_1_1
spine_2_1
spine_2_2
core_1_1
core_1_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_1
leaf_2_2
A
C
Z
W
M
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
VNI: 5010, VLAN ID 10
Prefix: 10.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 10.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 10.30.0.0/16
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
lo: 192.168.0.2/32
leaf_1_2
leaf_1_1
lo: 192.168.0.3/32
lo: 192.168.0.1/32
lo: 192.168.0.4/32
add leaf_1_2 in the lab.conf file
  the proper metadata (IPv6, multipath, image) are already declared
  define the machine interfaces (follow the grey numbers in the figure! )
2
1
0

## Slide 44: task 1: complete the topology
write server_2_1 “.startup” file
  it needs to be configured with VLAN tagging/untagging
    it must be able to forward VLAN=30 from/to container_2_1_1
  hint: the configuration is similar to server_2_2, you might “take a look” and adjust it!
AF
AA
AB
spine_1_2
spine_1_1
spine_2_1
spine_2_2
core_1_1
core_1_2
server_1_1
server_1_2
server_2_1
server_2_2
leaf_2_1
leaf_2_2
A
C
Z
W
M
O
L
N
K
E
B
D
Q
R
S
T
I
G
H
J
AS64512
AS64514
AS64513
AS64515
AS64516
AS64517
AS64518
AC
AD
1_1_1
1_1_2
1_1_3
1_2_2
1_2_1
2_1_1
AE
2_2_1
VNI: 5010, VLAN ID 10
Prefix: 10.10.0.0/16
VNI: 5020, VLAN ID 20
Prefix: 10.20.0.0/16
VNI: 5030, VLAN ID 30
Prefix: 10.30.0.0/16
.0.1
.0.2
.0.1
.0.1
.0.2
.0.2
.0.3
lo: 192.168.0.2/32
leaf_1_2
leaf_1_1
lo: 192.168.0.3/32
lo: 192.168.0.1/32
lo: 192.168.0.4/32
add server_2_1 in the lab.conf file
  the proper image is already declared
  define the machine interfaces (follow the grey numbers in the figure! )
1
0

## Slide 45: start the lab
open a terminal
enter the lab directory (cd lab_directory)
run kathara lstart

## Slide 46: task 2: verifying connectivity
let’s verify the reachability between containers
focus on container_1_2_1
  send a ping towards container_2_1_1:
  ping 10.30.0.2
  is the ping replying?
focus on container_1_2_2
  send a ping towards container_1_1_3:
  ping 10.20.0.1
  is the ping replying?

## Slide 47: task 3: analyzing EVPN-BGP
let’s analyze EVPN-BGP control plane
focus on container_1_1_1
  send a ping towards container_2_2_1 → ping 10.10.0.3
focus on container_1_1_3
  send a ping towards container_1_2_2 → ping 10.20.0.2
while the pings are going, focus on leaf_1_1
  enter the FRRouting control plane → vtysh

## Slide 48: task 3: analyzing EVPN-BGP
let’s analyze EVPN-BGP control plane
while the pings are going, focus on leaf_1_1
  in the BGP control plane, let’s check the EVPN routes:
  show evpn mac vni all
  which entries are displayed?
  can you explain the meaning of each column of each row?
    to which interface each MAC belongs to?
    is the VNI<->VLAN ID mapping working?

## Slide 49: task 4: analyzing VXLAN in action!
let’s analyze the VXLAN encapsulation in action
focus on container_1_1_1
  send a ping towards container_2_2_1 → ping 10.10.0.3
now, let’s focus on server_1_1
  start a tcpdump on the interface towards collision domain AA:
  tcpdump -i <iface> -c 8 -w /shared/server_1_1_AA.pcap
  it creates a pcap file in the /shared folder of the device
    that is mapped to the shared folder in your host’s lab directory
  tcpdump stops after 8 packets (-c 8 argument)

## Slide 50: task 4: analyzing VXLAN in action!
in the lab directory, go into the shared folder and open the server_1_1_AA.pcap file with Wireshark
  which packets do you see?
  are they encapsulated?
  what are the src IP and the dst IP?
    to which interfaces are they assigned?

## Slide 51: task 4: analyzing VXLAN in action!
let’s analyze the VXLAN encapsulation in action
while ping is still running, on server_1_1
  start a tcpdump on the interface towards collision domain C:
  tcpdump -i <iface> -c 8 -w /shared/server_1_1_C.pcap
open the server_1_1_C.pcap file with Wireshark
  which packets do you see?
  are they encapsulated? (pay attention here! )
    if yes, with which protocol?
    with what identifier?

## Slide 52: task 4: analyzing VXLAN in action!
let’s analyze the VXLAN encapsulation in action
while ping is still running, on leaf_1_1
  start a tcpdump on the interface towards collision domain A:
  tcpdump -i <iface> -c 8 -w /shared/leaf_1_1_A.pcap
open the leaf_1_1_A.pcap file with Wireshark
  which packets do you see?
  are they encapsulated?
    if yes, with which protocol?
    with what identifier?
    can you list all the IPs in the packet? (hint: they are more than two!)

## Slide 53: task 4: analyzing VXLAN in action!
let’s analyze the VXLAN encapsulation in action
while the ping is still running, perform the same analysis on the downward path
  dump leaf_2_2 interface on collision domain N
  dump server_2_2 interface on collision domain W
  dump server_2_2 interface on collision domain AF
analyze how the packets are decapsulated towards container_2_2_1

## Slide 54: task 5: container migration
let’s simulate a container migration to study how EVPN-BGP redistributes MAC addresses in the data center
we focus on migrating container_1_1_1
by checking the control plane of leaf_1_1
  the MAC address of container_1_1_1 is learned as local
    if not, send a ping towards container_2_2_1 to refresh the entry

## Slide 55: task 5: container migration
now, let’s migrate the container
open the lab.conf file and change the collision domain of container_1_1_1 interface 0 from AA to AF
  this will move the container into server_2_2
restart container_1_1_1
  to restart a single machine in a lab, run:
    kathara lrestart <machine_name>
    in this case: kathara lrestart container_1_1_1

## Slide 56: task 5: container migration
after migrating, focus on container_1_1_1 and run a ping towards container_1_1_2
check the EVPN-BGP control plane of leaf_1_1
  what happened to the VXLAN entry of container_1_1_1?
check the EVPN-BGP control plane of leaf_2_2
  is there any VXLAN entry for container_1_1_1?
  how is that learned? locally or remotely?

## Slide 57: task 5: container migration
restore the lab
  open the lab.conf file and change again the collision domain of container_1_1_1 interface 0 from AF to AA

## Slide 58: stop the lab
open a terminal
enter the lab directory (cd lab_directory)
run kathara lclean